## Slide 1: Build Your Own IoT!
Fun With a Raspberry Pi
By A.J. Fisher For the Perth Data Engineering Meetup
21/02/2024

## Slide 2: Agenda
Presentation Purpose
Quick Definitions
Project Inspiration
Hardware
Software / Pipeline
Next Steps to IoT
The Real World
Conclusion
Questions

## Slide 3: Project goals
Assemble a basic EL(T) streaming data pipeline that can be used for IoT applications
Encourage newcomers – anyone can build a streaming data pipeline!
Get closer to the bare metal
Share something I had a lot of fun doing

## Slide 4: Quick Definitions
IoT – Internet of Things
  Physical “Things” meet digital
  May involve device control
  Estimated 29 BILLION devices by 2030!
Streaming Data Pipeline
  Get data every 1 second
  Send / receive in the cloud continuously
Source
Source 1
Source 2

## Slide 5: WHY? Introduction to pi

## Slide 6
Temperature sensor
TAG: PIPE1XXTEMP01
25°C
1
2
3
4
Timestamp | PIPE1XXTEMP01
14-Feb-24 14:05:48 | 21
14-Feb-24 14:15:48 | 22
14-Feb-24 14:25:48 | 23
14-Feb-24 14:35:48 | 25
14-Feb-24 14:45:48 | 24
14-Feb-24 14:55:48 | 23
14-Feb-24 15:05:48 | 22
Engineers typically interact with batch data

## Slide 7: PI Demo – dashboard and excel

## Slide 8: Most Importantly…
Timestamp | RASPB-PIE-003
14-Feb-24 14:01:50 | DELICIOUS
14-Feb-24 14:11:50 | DELICIOUS
14-Feb-24 14:21:50 | Just ok I guess
14-Feb-24 14:31:50 | DELCIOUS
14-Feb-24 14:41:50 | DELICIOUS
Pie Data

## Slide 9: hardware

## Slide 10: Meet the team
SENSOR: solar panel
Translator: Analog-to-Digital-converter (ADC)
SERVER: Raspberry pi

## Slide 11: Full setup

## Slide 12: Notes on hardware
Where can I get ALL THIS hardware?
All project hardware can be acquired from Altronics in Northbridge!
174 Roe Street, Northbridge WA 6000
Altronics N0720 0.75W Mini Solar Panel
Adafruit ADS1115 16 Bit ADC
Raspberry Pi 4 Model B 4GB
“But I’ve never done electronics before!”
You can do it!
A.J. started with nothing too
Having a friend with an electrical engineering background is nice but…
LOTS of YouTube videos in the electronics community
Soldering can be tricky

## Slide 13: Software and data pipeline

## Slide 15
Ext
Read a voltage value from the solar panel
Extract

## Slide 16
Read a voltage value from the solar panel
?
Extract

## Slide 17
Library
Extract

## Slide 18: Sending the message
Measure and send voltage each 1 second
Serialised JSON message:
{
"connection_ok": True,
"panel_producing": "SOLAR_PANEL_1",
"voltage_volts": voltage,
}
Schema registry enabled
Actually measured each second
Not measured. Dummy values.
Mimics “real” reading

## Slide 19
Kafka producer: send voltage reading to Kafka in the cloud
Extract

## Slide 20
Kafka producer: send voltage reading to Kafka in the cloud
?
Extract

## Slide 21
Course
Extract

## Slide 22
Kafka in the cloud. Which cloud?
Extract

## Slide 23: Choosing a Cloud: Focusing on Data, Not Infrastructure
Cloud– can be a lot for beginners
Want something beginner friendly
Managed Kafka - data, not infrastructure
Expensive… BUT great for hobby, rapid prototyping & sizing
VS

## Slide 24
Store data for analysis
Store data for analysis
Extract
Load

## Slide 25
Load
Extract

## Slide 26
Kafka consumer for
app / analysis
Load
Extract

## Slide 27
Load
Extract

## Slide 28
Load
Extract

## Slide 29
Load
Extract
P
Transform
Convert volts to watts

## Slide 30
Load
Extract
P
Transform
Convert volts to watts
Transform?

## Slide 31
Load
Extract
P
Transform
Convert volts to watts
Transform?
Transform?

## Slide 32
Load
Extract
P
Transform
Convert volts to watts
Transform?
Transform?
Transform?

## Slide 33: NEXT STEPS TO IoT

## Slide 34: PART ONE: THE Journey so far
Local server
Downstream consumer
(On central server)
Data archive

## Slide 35: Step TWO: REVERSE PIPELINE WITH ACTUATION
Central server
Local server
Digital actuator
(variable resistance
potentiometer)

## Slide 36: Step Three: Build the presentation layer
Central server
Local server
Digital actuator
(variable resistance
potentiometer)

## Slide 37: Step four: Build a simple application interface
Central server
Local server
Digital actuator
(variable resistance
potentiometer)
Use Django to set
the potentiometer
resistance

## Slide 38: The real world

## Slide 39: The real world: project symphony
Project Symphony
Source

## Slide 40: Conclusion
We learned a bit about PI
Built a basic streaming data pipeline that can be used for IoT applications
Anyone can build a streaming data pipeline
Building data pipelines is fun

## Slide 41: Thank you!
AJTheDataGuy@gmail.com
https://www.linkedin.com/in/ajfisher2/

## Slide 42: APPENDIX A: Tests

## Slide 43: tests
Mix of unit and integration tests
Unit test example
  Is this schema string valid JSON?
Integration tests
  Get ADC channel, get voltage value
Lingering Challenges:
Hardware – loose connections
Pytest not failing on server timeout
"""{"$id": "https://github.com/AJTheDataGuy/myURI.schema.json",
"$schema": "https://json-schema.org/draft/2020-12/schema#",
"additionalProperties": false,
"description": "JSON Schema definition for solar panel voltage data",
"properties": {
"connection_ok": {
"description": "Adding a boolean just for fun. Represents whether the panel is connected properly or not.",
"type": "boolean"
},
"panel_producing": {
"description": "Defines which solar panel is sending the message (only 1 in this hobby project)",
"type": "string"
},
"voltage_volts": {
"description": "Voltage from the panel in volts",
"type": "number"
}
},
"title": "SolarPanelVoltageSchema",
"type": "object"
}"""